## Slide 1: Day 02 - Memory & Performance
How memory layout affects our code
09/05/25

## Slide 2: Overview
We’ll cover:
How computers carry out instructions
How memory is organized across a computer
How data moves through a computer
With computers, there’s always more detail and caveats you can dive into.
We’ll keep this at a moderate level of detail.
Notes: Data movement and access is a recurring theme

## Slide 3: von Neumann Architecture
The design framework used by most modern computers
Memory stores both program instructions and data
Processing unit executes instructions on the data
Processing cycle:
Fetch data
Execute instructions
Store result data

## Slide 4: Processing Cycle
Example:
c = a + b
Fetch (load) the value of a
Fetch the value of b
Execute “add” operation on a and b
Store the result to the variable c

## Slide 5: Processing Cycle
Main Memory
Central Processing Unit
Control Unit (CU)
What are my instructions?
Here’s your instructions
Instructions:
c = a + b
Data:
a b
Registers
c = a + b
Notes: Remember the von Neumann architecture
Registers are smallest memory

## Slide 6: Processing Cycle - Fetch
Main Memory
Central Processing Unit
Control Unit (CU)
I need to fetch a
Instructions:
c = a + b
Data:
a b
Registers
a
Ok, here’s a
c = a + b

## Slide 7: Processing Cycle - Fetch
Main Memory
Central Processing Unit
Control Unit (CU)
Also I need b
Instructions:
c = a + b
Data:
a b
Registers
b
a
c = a + b

## Slide 8: Processing Cycle - Execute
Main Memory
Central Processing Unit
Control Unit (CU)
Time to add
Instructions:
c = a + b
Data:
a b
Arithmetic Logic Unit (ALU)
Registers
a
c = a + b
b

## Slide 9: Processing Cycle - Store
Main Memory
Central Processing Unit
Control Unit (CU)
Instructions:
c = a + b
Data:
a b
Arithmetic Logic Unit (ALU)
Here’s the result
c
Registers
a
c = a + b
b
c

## Slide 10: Why does it matter?
Scientific software performance depends on data movement
Computers try hard to be efficient - we can leverage this!
Goal: Understand how leveraging data efficiency makes for faster code

## Slide 11: Memory Hierarchy
Registers
Random Access Memory (RAM)
Size (bytes)
Numbers based on Intel Sandy Bridge assuming 3.6 GHz CPU (ca. 2012); The Science of Computing, Victor Eijkhout
192
2G
Latency (nanoseconds)
63.9 - 100
~ 0
Better Performance
More Storage
Notes: CPU requesting memory in registers is fast. Requesting memory in RAM is slow.

## Slide 12: Data Reuse
Registers
Random Access Memory (RAM)
Consider:
c = a + b
d = 2*a + c
a
b
c
a
b
c
Notes: CPU does it's "work" in the registers
Values probably still in register

## Slide 13: Data Reuse
Registers
Consider:
c = a + b
d = 2*b + c
b
c
a
Random Access Memory (RAM)
a
b
c
Notes: Values probably still in register
Go back to CPU diagram

## Slide 14: Data Reuse
Main Memory
Central Processing Unit
Control Unit (CU)
Instructions:
c = a + b
d = 2*b + c
Data:
a b c
Arithmetic Logic Unit (ALU)
d
Registers
a
d = 2*b + c
b
c
I already have the data I need
d
Notes: Go back to CPU diagram.
Don’t need to request from main memory

## Slide 15: Drawback
CPU registers are very small (only a few hundred bytes)
Have to hold both active data and instructions
It’s very hard to keep data in registers for re-use
Are we stuck going to main RAM memory every time?
c = a + b
Other stuff
d = 2*b + c
Registers
y
z
x
Random Access Memory (RAM)
a
b
c

## Slide 16: Memory Hierarchy
Central Processing Unit
Control Unit (CU)
Arithmetic Logic Unit (ALU)
Registers
L1 Cache
Registers
L1 Cache
Random Access Memory (RAM)
???
Notes: Is there anything else in the hierarchy?

## Slide 17: Memory Hierarchy
Central Processing Unit
Core
Control Unit (CU)
Arithmetic Logic Unit (ALU)
Registers
L1 Cache
Registers
L1 Cache
Random Access Memory (RAM)
???
Notes: This is no longer the CPU

## Slide 18: Modern Multi-Core CPUs
Central Processing Unit
Core
Control Unit (CU)
Arithmetic Logic Unit (ALU)
Registers
L1 Cache
Modern CPU
Core
Core
Core
Core
L2 Cache
Controllers

## Slide 19
Intel Core 2 Duo (ca. 2006)
Intel Xeon “Tulsa” (ca. 2006)
Notes: Can also have L3 cache!

## Slide 20: Memory Hierarchy
Registers
L1 Cache
L2/L3 Cache
Random Access Memory (RAM)
“Disk” Memory
Latency (nanoseconds)
63.9 - 100
~ 0
Better Performance
Size (bytes)
192
2G
More Storage
32k
256k / 2M
1.1
3.3 / 7.2
Numbers based on Intel Sandy Bridge assuming 3.6 GHz CPU (ca. 2012); The Science of Computing, Victor Eijkhout

## Slide 21: Memory Hierarchy
Registers
L1 Cache
L2/L3 Cache
Random Access Memory (RAM)
c = a + b
a, b
c
Notes: So far this seems like more work
A copy at every level

## Slide 22: Memory Hierarchy
Registers
L1 Cache
L2/L3 Cache
Random Access Memory (RAM)
Some time later…
d = 2*b + c
b, c
d

## Slide 23: Review so far…
Processors execute instructions on data in a “fetch, execute, store” cycle.
Memory is organized as a hierarchy with data copied between levels.
Levels trade-off between storage capacity and speed.
The hierarchy makes it easier to reuse data and avoid data transfer.
Registers
L1 Cache
L2/L3 Cache
Random Access Memory (RAM)
For current instructions
One per CPU core
On CPU die, shared by cores
Current program instructions and data
Long-term storage; must explicitly access
Better Latency
More Storage
“Disk” Memory

## Slide 24: Exercise
A CPU core needs to fetch data.
  Thinking about the memory hierarchy, where will it first look for the data it needs?
  If the data isn’t in that first location, where will it look next?
A CPU core is trying to fetch data for “y = m*x + b”. The value for “x” was just used for the most recent set of instructions and is still in the register. The variable “m” was last updated a while ago and is still in L2 cache. Variable “b” is only in RAM.
  Diagram the movement (if any) of x, m, and b through the memory hierarchy.
  Which levels of the memory hierarchy have a copy of variables m and b?

## Slide 25: How Does Memory Work?
We’ll cover:
How information is stored in memory
How data moves through a computer (in more detail)
How we can exploit data movement for better performance

## Slide 26: Memory Addresses
Memory is referenced with addresses, like lots on a street.
Addresses get assigned to variables, like new houses being built
“Computer Memory, Variables, Variable Types, Arrays and Structures,” Herbert J. Bernstein
http://www.bernstein-plus-sons.com/.sjcny/Computer_Memory.html
Notes: Lot aka parcel

## Slide 27: Memory Addresses
Memory is referenced with addresses, like lots on a street.
Addresses get assigned to variables, like new houses being built
Houses can be of varying sizes and even occupy multiple lots.
Variables, too, can span multiple addresses.
Variable structure is defined by its type
“Computer Memory, Variables, Variable Types, Arrays and Structures,” Herbert J. Bernstein
http://www.bernstein-plus-sons.com/.sjcny/Computer_Memory.html
Notes: A house metaphor? In this economy??
Lot aka parcel

## Slide 28
pop | houses | mv_in | mv_out | n_dogs | n_cats | n_birds | n_other
1000 | 1004 | 1008 | 1012 | 1016 | 1020 | 1024 | 1028
75 | 57 | 3 | 8 | 32 | 46 | 2 | 7
Address
Value
Variable
Notes: Note “skip” in addresses

## Slide 29: Cache Lines
Data is copied as consecutive lines of addresses, called cache lines
Variables near each other in memory are transferred at the same time
Advantage: variables we may need next already have their data available!
Notes: Why does memory structure matter?
Example: Cache line covers 16 addresses

## Slide 30
RAM
Address
pop | houses | mv_in | mv_out | n_dogs | n_cats | n_birds | n_other
1000 | 1004 | 1008 | 1012 | 1016 | 1020 | 1024 | 1028
75 | 57 | 3 | 8 | 32 | 46 | 2 | 7
Value
Cache
houses | mv_in | mv_out | n_dogs
57 | 3 | 8 | 32
CPU
What’s the value for “houses”?
Great! What’s “n_dogs”?
What happens if the CPU requests “n_cats”?
Variable
Data is copied as consecutive lines of addresses, called cache lines
Notes: Why does memory structure matter? Caching!
Example: Cache line covers 16 addresses

## Slide 31: Lists, Tuples, & NumPy Arrays
These are all a form of Python “container”.
Containers are types that contain data of another type.
List Example
Array Example
Notes: Who isn’t familiar with NumPy arrays?
Difference between tuples and lists? NumPy arrays?

## Slide 32: NumPy Arrays
NumPy arrays are contiguous blocks of memory
Each block is the same size
arr = np.arange(5)
arr[0] | arr[1] | arr[2] | arr[3] | arr[4]
1112 | 1116 | 1120 | 1124 | 1128
0 | 1 | 2 | 3 | 4
Address
Value
Variable
Evenly spaced addresses

## Slide 33: NumPy Arrays
Size and type must be known ahead of time to allocate memory
Type tells us how big each “house” is
Size tells us how many “houses”
Notes: A “type” designed to hold data of other “types”

## Slide 34: Consider these arrays…
How much memory do we need?
Enough for…
Five integers
Seven integers
Seven floats
Notes: All approaches require size & type (even implicit)

## Slide 35: NumPy Arrays & Cache Lines
The structure of NumPy arrays makes them work well with cache lines!
arr = np.arange(5)
for item in arr:
print(item)
arr[0] | arr[1] | arr[2] | arr[3] | arr[4]
1112 | 1116 | 1120 | 1124 | 1128
0 | 1 | 2 | 3 | 4
One request to RAM pulls multiple values into the cache.
We can use them one after another without additional fetches to RAM.
Notes: Request one variable, get a line

## Slide 36: Lists
Lists are also contiguous blocks of memory
But lists can hold objects of any type, including other lists!
Memory blocks are not the same size
lst[0] | lst[1] | lst[2] | lst[3]
1300 | 1302 | 1306 | 1314
“a” | 4 | 2.5 | “c”
Address*
Value
Variable
* I made up the size of each block
lst = [“a”, 4, 2.5, “c”]
If lists worked like arrays:
Notes: Computers don’t handle this well!

## Slide 37: Pointers
Lists instead rely on pointers.
Pointers are a special type of variable whose value is the address of another variable somewhere else in memory
Address
Value
Variable
my_pointer
1001
3256
<no name>
3256
“hello”
Notes: Familiar for C/C++
Under the hood in Python (implemented in C)

## Slide 38: How lists really work
Address
Value
Variable
lst = [“a”, 4, 2.5, “c”]
lst[0] | lst[1] | lst[2] | lst[3]
1300 | 1302 | 1304 | 1306
1624 | 2986 | 3210 | 3244
Evenly spaced addresses :)
Address of actual data
<no name>
1624
“a”
<no name>
2986
4
<no name>
3210
2.5
<no name>
3244
“c”
Notes: Think: an array of pointers
Super flexible!

## Slide 39: Arrays vs Lists - Accessing Data
arr = np.arange(5)
print(arr[0])
lst = [“a”, 4, 2.5, “c”] print(lst[0])
Array entries are desired data
Fetch arr[0]
It’s our data! Print.
List entries are actually pointers; Data lives elsewhere
Fetch lst[0]
It’s a pointer! Dereference.
Fetch address saved to pointer lst[0]
It’s our data! Print.
Notes: Keep this up while pivoting to diagramming exercises.
Which has greater cache reuse?

## Slide 40: Review
Processors execute instructions on data in a “fetch, execute, store” cycle.
Memory is organized as a hierarchy
  Balances speed and capacity
Data is transferred through the hierarchy as consecutive blocks called “cache lines”
  Let’s us fetch data before we need it, if we’re clever
Variables are values associated with a memory address
A pointer is a special data type whose value is another address